## Slide 1: The influence of local optimised energy communities on the European electricity market
Christoph Loschan, Daniel Schwabeneder, Georg Lettner
(TU Wien – Energy Economics Group)
12. Internationale Energiewirtschaftstagung
Session 6C: Energy Communities III - 9.9.2021

## Slide 2: Overview
Introduction
1
2
2.2
Market Model
Energy Community Model
2.1
Model Formulation
Results
3

## Slide 3: Introduction - Motivation
Clean Energy for all Europeans
Renewable Energy Expansion
–> 2030: 32%
Renewable Energy Communities
Citizens Energy Communities
EAG & ElWOG

## Slide 4: Introduction – Energy Communities
Renewable Energy Communities
  Group of household & mid-sized companies
  Produce / store / sell RES-E
  Trade with external energy (store / sell)
  Objective: ecological, ecomomic, social benefits & financial gain
Citizien Energy Communities
  Not limited to RES-E
  Includes large companies
  No grid level restrictions
  Objective: non-profit

## Slide 5: Introduction – Energy Community
Research Question: What are the influences of ECs on the electricity market in terms of electricity generation costs and CO2 emissions?
External grid tariffs
[1]
Internal grid tariffs
Households form EC
PV systems, battery
Producer: smaller economic difference between self-consumption and feed-in
Consumer: Lower energy prices than external
Lower grid tariffs & fees

## Slide 6
EDisOn – Market Model
Minimising of the OV generation costs
Pricing through marginal costs of the power plants used
Day-ahead Market Price
Femto – Energy Community Model
Minimising the electricity costs of the energy community
Increased market procurement when market prices are low
Residual Demand
Model Formulation

## Slide 7: Model overview – nodes & connections
Min. OV costs (Max. social welfare)
(th. PP, RESE, storages)
365 x 1 day optimisation
Detailed power plant allocation
Transmission grid & DC loadflow
Market-model

## Slide 8: Model Formulation - Objective
365 x 1 Day-ahead optimisation
thermal generation
RESE
Storage usage
Not supplied energy
Market-model

## Slide 9: Model Formulation - Constraints
for all RES types
Demand compensation
in every balancing group
thermal PP
Market-model

## Slide 10: Model Formulation - Constraints
Technical &
Annual pattern storage constraints
Power exchange between
balancing groups
NTC limit
Market-model

## Slide 11: Model Formulation - Objective
EC-model
Minimisation of ECs operating costs
Market: Energy procurement & feed-in
External grid tariffs & fees
Internal grid tariffs & fees
EC: energy price
Model output -> market model

## Slide 12: Model Formulation - Constraints
EC-model
Demand Compensation
for each household
Local PV generation
EC Trade
PV Feed-in
Buy/Sell restriction

## Slide 13: Preliminary Results - Scenarios
ENTSO-E 2030 NT scenario
  Existing power plants and RES-E (100% net. RES-E in AUT)
  Electricity demand
3 Different scenarios (Austrias PV/Storage investments)
  „BAU“: Business-as-Usual: 9 GW PV / 2.9 GWh Battery (market)
  „market optimal“: 12 GW PV / 4.9 GWh Battery (market)
  „market & EC it. 1-5“: 9 GW PV / 2.9 GWh Battery (market) &
    3 GW PV / 2.0 GWh Battery (Community)

## Slide 14: Preliminary Results – EC Set-Up
8 Households per EC
Grid level 7
125000 ECs in Austria (-> 25 % of all Housholds)

## Slide 15: Preliminary Results: OV costs
Several Iterations ->
no significant difference
BAU vs. EC:
0.33 % cost reduction
BAU vs. market optimum:
0.46 % cost reduction
Delta Social Welfare: ~90 M€
EC savings: 50 M€

## Slide 16: Preliminary Results – EC cost savings
Less PV feed-in
Less ext. grid usage
267€ less grid tariffs & fees
128€ savings: PV & storage usage
6.6 % total

## Slide 17: Preliminary Results: OV CO2 emissions
BAU vs. EC:
-0.3 % emissions
BAU vs. market optimum:
-0.32 % emissions

## Slide 18: Preliminary Results: CO2 Austria
Lower emissions with ECs than in “market optimal”
Objective: Costs (CO2 price -> CO2)
Oil, Coal, Lignite < Gas usage
Austria 100 % net. RES-E
“Market optimal” more flexibilities (storages)
  More Gas in AT
  Less Coal NL and DE
  Less Lignite CZ and DE

## Slide 19: Ausblick
Danke!
This work is done in the BEYOND project.
The BEYOND project has received funding in the framework of the joint programming initiative
ERANet Smart Energy Systems, with support from the European Union's Horizon 2020 research and innovation programme and is an associated project within Green Energy Lab.
Christoph Loschan, Daniel Schwabeneder, Georg Lettner
(TU Wien – Energy Economics Group)
Aggregierte Teilnahme am Regelenergiemarkt
Veränderte Auslastung des Übertragungsnetzes
Einfluss von Leistungspreisen

## Slide 20: References
[1] Icons: Were designed by TU Wien ESEA (Source: https://gitlab.com/team-ensys/energy-system-icons)