## Slide 1: Investigating the demand side flexibility of the residential building stock
Philipp MASCHERBAUER, Lukas KRANZL
IEWT 2021
06.09.2021

## Slide 2
NewTrends – From Consumers to Prosumagers
Horizon 2020 project
  How do New Societal Trends affect energy demand?
  Work package 5 focuses on Prosumagers and big data (new data sources) in energy demand models related to the built environment
      Link to the project: https://cordis.europa.eu/project/id/893311
My objective:
How can active demand response measures of buildings with heat pumps (HP) in the residential sector affect the aggregate load profile on the national level?
  In this regard the potential storage of the thermal buildings mass is considered for every building
    Bottom-up energy supply optimization of a national building stock. In: Energy and Buildings 209, S. 109667. DOI: 10.1016/j.enbuild.2019.109667

## Slide 3
Method
Household
Country
Appliances
Dryer
Dish washer
Washing machine
Building
Type
Age class
Components
Space heating
Type of heating system
Thermal storage size
Scenario
Policy and economics: hourly electricity price and feed-in tariff
Weather: hourly radiation and temperature
Behavior: target indoor temperature, lifestyle
Optimization model
Reference model
Load profiles
Load profiles
comparison
PV
Size
 profile
Battery
Capacity
Space cooling
Type of cooling system
Hot water
Demand profile from HOTMAPS

## Slide 4
Perspective: household
Time resolution: hourly
Objective:
  minimize the operation cost (s.t. hourly demand profiles of electricity / heating / cooling / hot water)
Decision variables:
  hourly operation of technologies over one year
Method
Optimization model
Reference model
Perspective: household
Time resolution: hourly
Method of operation:
  PV generated electricity is used to cover demand
  Surplus of electricity from PV is stored
  If storages are full or not available, surplus is sold
  Appliances (dishwasher, washing machine, dryer) are started randomly throughout the day between 6 am and 9 pm.
  Thermal inertia is not utilized as storage

## Slide 5
5 representative single family houses taken from the building stock database of the “Invert/EELab” for the case of Austria
Building ID | Af [m2] | Hop [W/K] | Htr_w [W/K] | Hve [W/K] | Cm factor [J/K] | Am [m2] | Construction year | Number of buildings
1 | 154 | 203 | 86 | 43.595 | 213 505 | 3 | 1961-1970 | 21 451
2 | 163 | 208 | 97 | 46.189 | 213 505 | 3 | 1971-1980 | 97 729
3 | 166 | 144 | 77 | 46.938 | 213 505 | 3 | 1981-1990 | 145 126
4 | 170 | 121 | 69 | 47.964 | 181 194 | 2.8 | 1991-2000 | 208 914
5 | 170 | 95 | 54 | 47.964 | 114 415 | 2.5 | 2001-2008 | 110 345
Buildings
Parameters of the representative buildings for calculation of the 5R1C model explained in DIN ISO 13790
Af … usable area
Hop … heat transmission coefficients for the opaque building components
Htr_w … heat transmission coefficients for windows
Hve … heat transfer coefficient for ventilation
Cm … internal heat storage capacity of the building
Am … effective mass-related area

## Slide 6
Scenarios
1
2
3
4
5
10 kWp PV
5 kWp PV
No PV
No thermal storage
1500 l hot
water tank
No battery storage
7 kWh battery storage
Indoor set temperature:
“smart” Tmin=20°C+(Toutside – 20°C +12)/8
Tmax = 27°C
steady [20°C, 27°C]
Electricity price type:
fixed
variable

## Slide 7
Preliminary Results
A flat electricity price does not promote load shifting without storages
Utilizing the thermal mass shifts peaks but also results in higher energy demand (due to losses)
Week 8
Electricity from
the grid (kw)
Electricity from
the grid (kw)
fixed price
variable price
Building is preheated
Smart appliances

## Slide 8
Preliminary results
When storages and PV are implemented the electricity demand becomes volatile especially when the price is variable
Week 8
Electricity from
the grid (kw)
Electricity from
the grid (kw)
fixed price
variable price
Notes: Right now the heat pump has no restriction on load changing, these results will become less volatile when the heatpump is modeled more accurately in the further course of this research.

## Slide 9
Preliminary results
The scenario with a variable electricity price results in a higher total electricity demand (because of losses)
PV and thermal storages reduce the total amount needed from the grid
The scenario with a fixed electricity always results in lower electricity used from the grid
Fixed price results in slightly higher PV self consumption compared to variable price
PV…Photovoltaic, B…Battery storage, T…Thermal storage
 PV5B7T1500…PV: 5kWp, Battery storage: 7 kWh, Thermal storage: 1500 l
PV electricity self consumed (kwh)
(optimization - reference)
PV self consumption average difference between optimization and reference for different electricity prices
Electricity from the grid (kwh)
(optimization - reference)
Grid electricity consumption average difference between optimization and reference for different electricity prices
Preheating of buildings and use of battery
Storage result in higher losses

## Slide 10
Findings
Optimization will always result in lower Electricity demand (fixed price)
Variable electricity price results in large amounts of energy shifted and contrary to the fixed electricity price it will increase the electricity demand when no thermal storage and PV are available.
Even households without any kind of storage and PV can shift their demand considerably with their thermal mass
Outlook
Quantification of overall load shifting potential
Aggregation of load profiles to the whole building stock
Including the actual distribution of heating systems in the buildings as well as installed PV systems
Inclusion of investment costs
Development of different scenarios until 2050 by coupling this model with the building stock model „Invert“
Analyze cooling energy
Analyze effects in other countries
Conclusion and Outlook

## Slide 11: Thank you for your attention!
Philipp Mascherbauer
mascherbauer@eeg.tuwien.ac.at
Notes: Thank you for you attention! If you have any questions or feedback, I am happy to hear it