## Slide 1: Evaluation of energy autarky-optimal technology portfolio of a local energy system
Frida Revheim, Daniel Schwabeneder, Georg Lettner
TU Wien Energy Economics Group
revheim@eeg.tuwien.ac.at
IEWT 2021
08.09.21

## Slide 2
Introduction and motivation
Methodology
  Model development
  Use cases
Preliminary results
Further work
Introduction

## Slide 3: Idea and motivation
  Sector coupling could be part of a solution to reach GHG emission targets
    Green hydrogen and green heat
    Curtailment reduction
  Energy autarky: “conceptualized as a situation in which the energy services used for sustaining local consumption, local production and the export of goods and services are derived from locally renewable energy resources.” (Müller et al., 2011)
  Autarkic energy systems are able to lower their dependence on external energy systems
  Key motivational factors:
    Ensure continued implementation and operation of RES
    Reduce GHG emissions
    Enable energy autarky

## Slide 4: Methodology – model development
  Model development builds on energy cell from Johann project [1] and considers the energy demands of a household
  Investigated system includes both P2H and P2G technology
  Additional heat pump considered in one use case
  Remaining electricity and heat demand are met by heat and electricity bought from external sources

## Slide 5: Methodology – model development
  Johann energy cell developed by Elements Energy [2]
Battery for short-term electricity storage
Conversion to hydrogen for long-term storage by utilizing electrolyzer and H2 storage tanks
Fuel cell converts hydrogen back to electricity
Electricity is either used by customer or sold to electricity market
Excess heat from electrolysis and fuel cell processes are utilized to cover heat demand
Source: Elements Energy, https://www.elements-energy.at/

## Slide 6: Methodology – model development
  Optimization model of sector coupled system developed in Julia
  Currently optimizing system operation with regards to autarky – further development to perform portfolio optimization
  Aim: perform a portfolio optimization to evaluate the energy autarky-optimal technology portfolio of an energy system
  Preliminary results are based on current operational optimization model where objective is set to minimize external energy purchase

## Slide 7: Methodology – use cases
  Two different use cases investigated in addition to baseline
    Farmhouse
      Heat pump considered in addition to energy cell
    Riding stable
      No heat pump
    Baseline
      No energy cell
Baseline
No energy cell
Riding stable
Del > Dheat
No heat pump considered
Farmhouse
Del < Dheat
Additional heat pump

## Slide 8: Preliminary results – farmhouse use case
Overview of technology utilization in farmhouse use case
Majority of generated electricity is either fed into energy cell (electrolyzer + battery) or sold to the electricity market
Heat pump covers around 77 % of assumed heat demand

## Slide 9: Preliminary results – farmhouse use case
Degree of energy autarky increases under current assumptions
  70 % energy self-reliance achieved for electricity demand
    Majority of electricity demand met by electricity produced by PV
    Both short-term and seasonal storage utilized when needed
  84 % energy self-reliance achieved for heat demand
    Implementation of heat pump increases the degree of energy autarky related to meeting the heat demand
Chart: Electricity demand
Electricity produced by PV | 0.45355
Electricity from battery | 0.089277
Electricity produced by fuel cell | 0.16146
Chart: Heat demand
Heat produced by heat pump | 0.77135
Heat produced by electrolyzer | 0.026936
Heat produced by fuel cell | 0.038562

## Slide 10: Preliminary results – farmhouse use case
Significant GHG emission reduction potential
Implementing Johann energy cell results in
  47 % reduction of emissions related to covering the electricity demand
  68 % reduction of emissions related to covering the heat demand
Reduction potential depends on
  Size of technology utilized
  Emission factor of electricity mix
  Alternative fuel considered (natural gas)
Chart: Reduced GHG emissions due to energy cell [%]
| Electricity demand | Heat demand
 | 0.46796 | 0.68474

## Slide 11: Preliminary results – stable use case
Overview of technology utilization in riding stable use case
Utilizing the energy cell combined with PV significantly reduces the amount of external electricity bought
No heat pump implemented  majority of heat demand is met by excess heat from internal processes

## Slide 12: Preliminary results – stable use case
Degree of energy autarky increases under current assumptions
  94 % energy self-reliance achieved for electricity demand
    Majority of electricity demand met by electricity produced by PV
    Both short-term and seasonal storage utilized when needed
  97 % energy self-reliance achieved for heat demand
  No heat pump implemented in this use case
  Relatively low heat demand  excess heat from internal processes sufficient to meet heat demand
Chart: Heat demand
Heat produced by electrolyzer | 0.47839
Heat produced by fuel cell | 0.49569
Chart: Electricity demand
Electricity produced by PV | 0.49949
Electricity from battery | 0.11492
Electricity produced by fuel cell | 0.32728

## Slide 13: Preliminary results – stable use case
Chart: Reduced GHG emissions due to energy cell [%]
| Electricity demand | Heat demand
 | 0.8825 | 0.97408
Significant GHG emission reduction potential
Implementing Johann energy cell results in
  88 % reduction of emissions related to covering the electricity demand
  97 % reduction of emissions related to covering the heat demand
Reduction potential depends on
  Size of technology utilized
  Emission factor of electricity mix
  Alternative fuel considered (natural gas)

## Slide 14: Concluding remarks and further work
  Utilization of sector coupling concepts combined with short-term and seasonal electricity storage has the potential to
    reduce GHG emissions
    increase the degree of energy autarky
  Portfolio optimization is yet to be performed
  Further work
    Evaluate optimal system topology under consideration of different degrees of autarky
    Consider the possibility of having green hydrogen as output from the energy cell – as well as possible ways of utilization
    Investigate the impact of local policy levers on influential parameters (e.g. energy demand, available fuel options)

## Slide 15: References and acknowledgements
This work is done in the “Energy cell “JOHANN”” project [1] and is supported with the funds from the Climate and Energy Fund and implemented in the framework of the RTI-initiative “Flagship region Energy” within Green Energy Lab.
  [1] Energiezelle „JOHANN“, Green Energy Lab, https://greenenergylab.at/projects/energiezelle-johann/
  [2] Der Hybrid-Energiespeicher der Zukunft - JOHANN, Elements Energy, https://www.elements-energy.at/
  [3] Matthias Otto Müller, Adrian Stämpfli, Ursula Dold, Thomas Hammer (2011). Energy autarky: A conceptual framework for sustainable regional development. Energy Policy, 39(10), 5800-5810. https://www.sciencedirect.com/science/article/pii/S0301421511003028

## Slide 16
Frida Revheim
TU Wien
Energy Economic Group, EEG
Gußhausstraße 25-29 / E370-3
1040 Vienna, Austria
Email: revheim@eeg.tuwien.ac.at
Web: http://www.eeg.tuwien.ac.at
Thank you!