## Slide 1: Flexibility Potential of a Generic Cold Warehouse IEWT 2021, PhD day, TU Wien
Ehsan Khorsandnejad
Oberhausen, 07.09.2021

## Slide 2: flexibility
Definition:
  The ability to adjust the performance of the energy system in reaction to an external signal over a period [1]
Quantification:
  Goal-based quantification of flexibility potential through mathematical optimization of the operation (MILP)
  Comparison between normal operation and optimized operation
 Example: Electricity purchase costs

## Slide 3: Evaluation of flexibility potential
By means of metrics:
    Higher  higher load shift
  Electricity costs
  Energy consumption
  CO2-Emission
  Load change: any change in the power consumption of the refrigeration system

## Slide 4: Goals, Objective functions and external signals
Minimization of CO2-Emissions
  Penalty costs for CO2-factor in electricity grid
  Negative penalty costs for proportion of electricity from wind and PV-plants in the grid
   : real or penalty costs
   – Power consumption
   – time step
Minimization of electricity purchase costs via electricity prices from EPEX Spot
Peak shaving
Integration of local RES via a 750 kW PV-plant
  Negative penalty costs
: work price and : power price

## Slide 5: Examples for external signals
Electricity price data from EPEX Spot 2019
Minimization of CO2-Emissions
Source: [1]
Sources: [3, 4]

## Slide 6: Configuration of a cold supply system
Energy sources
Conventional
Power plants
Central RES
Local RES
Fuels
Different heat sources
CHP
Cold energy
Cold storage
Heat
Electricity
Energy
Conversion
VCRS
ARS
Energy storage
Energy Consumers
Heat storage

## Slide 7: Optimization model
Tool:
  Open Energy Modelling Framework (EOMOF)
  Optimization type: MILP
  For the year 2019
  Time resolution: 15-minute intervals
  Rolling horizon: 24-hour periods
Programming language:
  Python
PV-plant
Electricity grid
VCRS
Deep Cooling
1
2
3
4
2
3
1
4
VCRS
Normal Cooling
Inherent
cold storage
Ice storage
Deep Cooling
Normal Cooling

## Slide 8: Detail degree of models
For ARS
  Minimum run-time
  Influence of ambient temperature
  Partial load behaviour
  Cold start
  Warm start
For VCRS
  Minimum run-time
  Influence of ambient temperature
  Partial load behaviour
  Stepwise operation
  Maximum number of starts
  Re-cooling
Energy storage
  Energy loss – based on storage filling level
  Energy input and output loss
  Energy input and output capacity

## Slide 9: Refrigeration demand
Daily pattern
Yearly pattern
Source: [5]
Source: [5]
Maximum refrigeration demand:
×

## Slide 10: Results

## Slide 11: Considerations and conclusions
Considerations
  Analyse the local PV-plant separately
  Only is considered for electricity purchases costs
Conclusions excluding the integration of PV-plant:
  Peak shaving resulted in higher electricity purchase costs
  Peak shaving was not achieved by other goals
  Minimization of CO2 –emissions was minimal
  Load change corresponds to the flexibility factor
  Energy consumption increased drastically for minimization of electricity purchase costs
  The optimization results for the two objective function used to minimize of CO2 –emissions were largely similar

## Slide 12
Thank you for your attention

## Slide 13: KONTAKTDATEN
Fraunhofer UMSICHT Osterfelder Straße 3 46047 Oberhausen, Germany E-Mail: info@umsicht.fraunhofer.de Internet: http://www.umsicht.fraunhofer.de
M.Sc. Ehsan Khorsandnejad
Doktorand und Wissenschaftlicher Mitarbeiter
Telefon: +49 208 / 8598-1518 E-Mail: Ehsan.Khorsandnejad@umsicht.fraunhofer.de

## Slide 14: Referenzen
© Fraunhofer UMSICHT | Bernd Röttgers
[1] EPEX Spot (2019): Market Data. Online verfügbar unter https://www.epexspot.com/en/market-data?data_mode=map&modality=Auction&sub_modality=DayAhead&product=60&de-livery_date=2021-03-30&trading_date=2021-03-29, zuletzt geprüft am 29.03.21.
[2] Weiß, Tobias; Rüdisser, Daniel; Reynders, Glenn (2019): Tool to evaluate the Energy Flexibility in Buildings. A short manual. Hg. v. Energy Technology Network. Energy in Buildings and Communities Programme.
[3] Agora Energiewende (2019): Strompreis und Emissionen. Online verfügbar unter https://www.agora-energiewende.de/service/agorameter/chart/power_price_emission/01.01.2019/31.12.2019/, zuletzt geprüft am 04.03.2021.
[4] Bundesnetzagentur (Hg.) (2019): Markttransparenzstelle für den Großhandel mit Strom und Gas; Aufgaben nach REMIT; SMARD-Strommarktdaten.
[5] Grein, Arne; Pehnt, Martin; Markus, Duscha; Holger, Kellerbauer (2009): Modellstadt Mannheim in der Metropolregion Rhein-Neckar, Mannheim.

## Slide 15: Referenzen
© Fraunhofer UMSICHT | Bernd Röttgers
[1] Thomas Langrock, Siggi Achner, Christian Jungbluth, Constanze Marambio, Armin Michels, Paul Weinhard, Bastian Baumgart, Achim Otto (2015): Potentiale regelbarer Lasten in einem Energieversorgungs-system mit wachsendem Anteil erneuerbarer Energien.
[2] VDE-Studie (2012): Lastverschiebungspotenziale in Deutschland. "Demand Side Integration".
[3] B. K. Nalini, M. Eldakadosi, Z. You, M. Zade, P. Tzscheutschler and U. Wagner, "Towards Prosumer Flexibility Markets: A Photovoltaic and Battery Storage Model," 2019 IEEE PES Innovative Smart Grid Technologies Europe (ISGT-Europe), 2019, pp. 1-5, doi: 10.1109/ISGTEurope.2019.8905622.
[4] Weiß, Tobias; Rüdisser, Daniel; Reynders, Glenn (2019): Tool to evaluate the Energy Flexibility in Buildings. A short manual. Hg. v. Energy Technology Network. Energy in Buildings and Communities Programme.
[5] Bauknecht, Dierk; Heinemann, Christoph; Koch, Matthias; Ritter, David; Harthan, Ralph; Sachs, Anja et al. (2016): Systematischer Vergleich von Flexibilitäts- und Speicheroptionen im deutschen Stromsystem zur Integration von erneuerbaren Energien und Analyse entsprechender Rahmenbedingungen. Hg. v. Öko-Institut e.V. und Energynautics GmbH. Freiburg, Darmstadt.
[6] EPEX Spot (2019): Market Data. Online verfügbar unter https://www.epexspot.com/en/market-data?data_mode=map&modality=Auction&sub_modality=DayAhead&product=60&de-livery_date=2021-03-30&trading_date=2021-03-29, zuletzt geprüft am 29.03.21.
[7] Agora Energiewende (2019): Strompreis und Emissionen. Online verfügbar unter https://www.agora-energiewende.de/service/agorameter/chart/power_price_emission/01.01.2019/31.12.2019/, zuletzt geprüft am 04.03.2021.
[8] Bundesnetzagentur (Hg.) (2019): Markttransparenzstelle für den Großhandel mit Strom und Gas; Aufgaben nach REMIT; SMARD-Strommarktdaten.
[9] Grein, Arne; Pehnt, Martin; Markus, Duscha; Holger, Kellerbauer (2009): Modellstadt Mannheim in der Metropolregion Rhein-Neckar, Mannheim.