## Slide 1: Agent-based simulation of neighbourhood-level integrated retrofitting adoption
Ardak Akhatova
Supervisors:
Lukas Kranzl, TU Wien
Reinhard Haas, TU Wien
Energy Economics Group, TU Wien
12.IEWT, 08.09.2021, Energie in Gebäuden II

## Slide 2: Outline of the presentation
Introduction
  Motivation
  Background
  Research aim
Methodology – Agent-based model concept
Preliminary results (Verification) and discussion
Conclusion
  Limitations and outlook

## Slide 3: Motivation Need to stimulate energy-efficient building retrofitting (EER)
Despite numerous policy incentives [1], the rate of energy-efficient renovation/retrofitting (EER) in Europe is very low (0.4-1.2%) [2].
Energy-efficient retrofits (EER) of buildings, including:
  building envelope insulation
  improvement of heating systems
  integration of renewable energy systems (RES)
are necessary measures to reduce energy demand and the related emissions attributed to buildings [2].
More holistic neighbourhood-scale approaches could be a promising avenue in exploring how to stimulate EER.
In line with:
  IEA EBC Annex 75: Building Renovation at District Level
  Positive Energy Districts
[1] Wilson et al (2015). Why do homeowners renovate energy efficiently? Contrasting perspectives and implications for policy. DOI: 10.1016/j.erss.2015.03.002
[2] European Commission. (2019). Comprehensive study of building energy renovation activities and the uptake of nearly zero-energy buildings in the EU Final report. www.navigant.com
Notes: Benefits from energy savings might be uncertain or poorly explained and understood, especially by the end-users. They can be difficult to measure and monetise.
Buildings are responsible for approximately 40% of EU energy consumption and 36% of the greenhouse gas emissions. (Energy performance of buildings directive)
At least 75% of today’s buildings will still exist by 2050 [1]
Examples of policies at place (Wilson et al., 2015):
energy audits and assessments;
energy performance certificates or ratings at the point of sale;
financial incentives and capital support (including grants, subsidies, tax credits, low interest loans, and third party financing);
certification and training of contractors;
community or neighbourhood renovation schemes (collective procurement, support for vulnerable or low income households);
marketing and information campaigns.

## Slide 4: Background Integrated retrofitting on a neighbourhood level
Integrated retrofitting
  renovation packages, i.e. combination of single measures (more ambitious and “complex, fragmented offers can be integrated into offers of higher value proposition” [3]).
Neighbourhood-level retrofitting
  Many benefits: driving down the costs by the economies of scale, awareness, more social acceptance and neighbourhood engagement.
Main stakeholders
  Homeowners – decision-makers about EER
  Intermediary actors – facilitators
Agent-based model as a main method: Socio-technical system, interaction between stakeholders
[3] Boza-Kiss, B. and Bertoldi, P. (2018). One-stop-shops for energy renovations of buildings. JRC Science for policy report.
Non-profit Organizations (the project Isol’action)
Neighbourhood authorities (e.g. redevelopment in Griesheim-Mitte, Frankfurt)
One-Stop-Shops
Market development team in the Energiesprong initiative.
Other private companies doing integrated building retrofitting (e.g. GreenHome)
Notes: Benefits from energy savings might be uncertain or poorly explained and understood, especially by the end-users. They can be difficult to measure and monetise.
Buildings are responsible for approximately 40% of EU energy consumption and 36% of the greenhouse gas emissions. (Energy performance of buildings directive)
At least 75% of today’s buildings will still exist by 2050 [1]
Examples of policies at place (Wilson et al., 2015):
energy audits and assessments;
energy performance certificates or ratings at the point of sale;
financial incentives and capital support (including grants, subsidies, tax credits, low interest loans, and third party financing);
certification and training of contractors;
community or neighbourhood renovation schemes (collective procurement, support for vulnerable or low income households);
marketing and information campaigns.

## Slide 5: Aims & Research questions Pathways to positive and net-zero energy districts via retrofitting
Research aim
To explore under which conditions retrofitting of whole neighbourhoods can take place.
Objective
To develop and present a simplified agent-based model (ABM) that simulates the adoption (i.e. ‘diffusion’) of specified retrofitting options by heterogeneous building owners (under a ‘hypothetical’ neighbourhood-level retrofitting program).
Rationale
Building owner agents are rational entities who ‘decide’ whether to implement ‘retrofitting packages’. Their decisions may be influenced by neighbouring homeowners (and intermediate actors).
Research Question
What levels of energy demand (and emission*) reduction can be achieved via neighbourhood-level integrated retrofitting program under different scenarios?
*To be explored in the further work
Notes: What socio-techno-economic conditions enable the integrated net-zero retrofitting of existing neighbourhoods towards PEDs?
  What are the retrofitting options (technology) available for building archetypes in a selected neighbourhood?
  What are the potential energy and cost savings from neighbourhood-level integrated net-zero retrofitting?
  Under which framework conditions (or policy interventions) would the housing providers and homeowners adopt retrofitting packages?
  What pathways should a neighbourhood take to become an affordable and inclusive Positive Energy District/Neighborhood and why?

## Slide 6: Methodology General model framework
Scenario 2
Scenario 1
Scenario n
…
Techno-economic analysis
Evaluate the final energy demand in building archetypes present in the selected neighbourhood
Design integrated retrofitting packages, calculate respective energy savings and costs
Agent-based simulation of the diffusion of retrofitting packages
Mesa on Python 3+
Results
Number of adopters
Packages adopted
Energy savings
Emission savings

## Slide 7: Methodology Core elements of agent-based modelling (in Mesa)
Agents (here: Homeowner Agents)
  Attributes (parameters & state variables)
  Decision-making strategy
    Interaction with other entities
Model (global level)
  Initialization: number of agents, input data
  Scheduling of the agent ‘actions’
Model
num_agents: integer
Num_agents_adopted: integer
Agent 0
-unique_id: integer
-interest: boolean
-budget: integer
-value_orientation: string
-prob_being_interested: float
-adoption_status: Boolean
-adopted package: object
-interest()
-affordability()
-decision()
Agent n
-adopted_package: object

## Slide 8: Methodology Homeowner agents’ decision-making framework
Three-stage decision process (based on synthesis of [4], [5])
Agent is ‘interested’ with a ‘prob_being_interested’ (e.g.= 0.3)
Agent filters out affordable retrofitting packages
Decision based on ‘value_orientation’
Financial agent (‘Fin’)
  (Eq. 2)
Environmental agent (‘Env’)
  (Eq. 1)
Social agents (‘Soc’)
  Rank adopted_packages according to quantity and take the #1
1.Interest
‘interested’: True or False
2.Affordability
Cost of ‘affordable_packages’ <= ‘budget’
3.Decision
‘Fin’: Max profit
‘Soc’: Imitate neighbours
‘Env’: Max energy savings
Based on ‘prob_being_interested’
[4] Arning et al (2020). The challenge of improving energy efficiency in the building sector: Taking an in-depth look at decision-making on investments in energy-efficient refurbishments.
[5] Wilson et al. (2018). Quantitative modelling of why and how homeowners decide to renovate energy efficiently

## Slide 9: Methodology Simulation process
Simulation starts
1. Initialization
2.2. Intermediary agent gives customized information on EER packages
4. Agent decisions are implemented and the state variables are updated
2.1. Homeowner agent is interested in EER?
2.2. Homeowner agent affords at least one EER package?
2.1. Homeowner agent withdraws the EER program
N
2.2. Homeowner agent withdraws the EER program
2.3. Intermediary agent ‘can’ advice further (or even influence the decision)*
2.3. Homeowner agent decides on the EER package?
3. Homeowner agent adopts one of the EER packages
(based on its own ‘goal’)
2.3. Homeowner agent withdraws the EER program
5. The results are collected
2.1. Intermediary agent ‘contacts’ n homeowner agents
Loop over agent
Loop over time
Simulation ends
Define simulation length
Load Building archetypes N of agents
Load retrofitting packages
Y
N
Y
N
Loop over agent
Loop over agent
Y
Number of adopters over time
Packages adopted by the end

## Slide 10: Methodology Scenarios and Inputs
3 test scenarios
  Budget (socio-economic status of the neighbourhood under study)
  Value orientation (social values of the population)
  Subsidies for homeowners (policy intervention)
 For now no real data, hence, the results are rather useful for the “verification”
Building archetype | Floor area | Energy initial | Energy type | Number
SFH1 (built before 1964) | 143 | 41570,1 | gas | 10
SFH2 (1965-1974) | 135 | 30456 | gas | 15
SFH3 (1975-1991) | 135 | 21411 | gas | 7
Table 1. Building archetypes selected in the illustrative example
Option | Name | Energy demand after [kWh/year] | Renewable energy gen. [kWh/year] | Cost [€/year] | Energy carrier after
1 | A | 37280,1 | 0 | 2860 | electricity
2 | B | 31560,1 | 1100 | 8580 | electricity
3 | C | 30130,1 | 1200 | 14300 | electricity
4 | D | 35850,1 | 0 | 4576 | electricity
5 | E | 30845,1 | 1000 | 12155 | electricity
6 | F | 28700,1 | 1300 | 14300 | electricity
Table 2. Input data on retrofitting packages for Building archetype SFH1
Energy type | Price per kWh
el_feedin | 0,5
el_retail | 0,13
gas | 0,077
Table 3. Input data on prices

## Slide 11: Results Impact of „budget“ on the retrofitting adoption
What is ‘budget’ available for EER?
 share of income of the neighbourhood under study
2 cases:
  lower budget
  (1,000-10,000)
At initialization (Timestep = 0)
Results (Timestep = 4)
Value orientations
Budget
# of adopted agents (per time step)
# of adopted retrofitting packages (total)

## Slide 12: Results Impact of „budget“ on the retrofitting adoption
What is ‘budget’ available for EER?
 share of income of the neighbourhood under study
2 cases:
  higher budget
  (10,000-30,000)
At initialization (Timestep = 0)
Results (Timestep = 4)
Value orientations
Budget
# of adopted agents (per time step)
# of adopted retrofitting packages (total)

## Slide 13: Results Impact of „Value orientation“
Only financial
Only environmental
Only social  nobody adopts
# of adopted agents (per time step)
# of adopted retrofitting packages (total)
# of adopted agents (per time step)
# of adopted retrofitting packages (total)

## Slide 14: Results Policy intervention: subsidies to all homeowner agents
2 levels of subsidy compared
  Lower (1,000)
  Higher (5,000)
subsidies only to lower income households?
# of adopted retrofitting packages (total)
# of adopted agents (per time step)
# of adopted retrofitting packages (total)
# of adopted agents (per time step)

## Slide 15: Conclusion
Model concept is implemented correctly
Added value/Novelty:
  new approach for analysing how retrofitting implementation could be stimulated (neighbourhood-level, intermediary agent, social and technical ‘foundation’)
Limitations (of the current version)
  Agent parameters & decision-making
  Intermediary agent’s decision-making strategy
  Abstraction of ‘interaction’ (to be defined better)
  Neighbourhood-specific scenarios
Outlooks/Next steps:
  Case study and data collection to parameterize the ‘attributes’ as well as validate the model
   survey and interview for neighbourhoods in Amsterdam & Frankfurt

## Slide 16: Thank you for your attention!
Questions?
Contact details:
ardak.akhatova@tuwien.ac.at